## Slide 1: PartInspect
A simulated ROS2 and Gazebo environment for automated quality inspection in manufacturing.

## Slide 2: The ACTORS
A CONVEYOR BELT
A VISION SYSTEM (made of 2 cameras alongside the conveyor belt)
A SOLENOID ACTUATOR
OBJECTS (cubes and cones)
Good parts (preserved)
Bad parts (pushed away from the solenoid)

## Slide 3: SYSTEM OVERVIEW

## Slide 4: VISION (& CHECK) Node
/camera1/image_raw
/vision/detection_result
/camera2/image_raw
/check/detection_result
The entire pipeline is applied to a specific Region of Interest (ROI),
to ensure that the object is fully visible in the image
VISION Node: detects defective parts and notifies the pusher
CHECK Node: detects defective parts that were not pushed away and notifies the controller
Both nodes receive images from simulated Gazebo cameras
Notes: Morphological opening cleans the image by deleting isolated pixels.
It is useful especially after a thresholding operation.
The polygon approximation is based on the Douglas-Peucker algorithm, and finds the polygon which contains all the object pixels.
It reduces the image to just the vertices of the borders, so it keeps the shape without considering all the image pixels (reducing the complexity).

## Slide 5: PUSHER Node
TRACKS MOTION of defective parts (once detected from the vision node)
  Actuation time is automatically computed based on the conveyor belt speed
  If belt speed changes between detection and actuation, the actuation time changes accordingly
Controls EXTENSION and RETRACTION of a simulated PID-controlled SOLENOID
  Retraction happens 500ms after the extension
/vision/detection_result
/config/belt_speed
/gazebo/pusher/cmd_pos

## Slide 6: CONTROLLER Node
CONVEYOR BELT controller
  Supports variable belt speed values
  Defalut belt speed is set 1 m/s
Continuously publishes belt speed to pusher node and commands simulated conveyor belt
  Continuous publishing ensures simulation stability and actuation accuracy
/check/detection_result
/config/belt_speed
/gazebo/conveyor_belt/cmd_vel

## Slide 7: Other ROS NODES
CLEANER Node: removes fallen object from the simulation
  Invokes a Gazebo service to delete objects
  Removal occurs 15 seconds after they reach the ground
DUMMY CAMERA Node: generates fake camera images
  Provides a mock interface for a Gazebo camera
  Enables system testing without a Gazebo simulation
/gazebo/spawned_objects/odometry
ros_gz_interfaces/srv/DeleteEntity
/camera1/image_raw

## Slide 8: CONCURRENCY
Notes: All nodes (a part from the dummy camera node) works at the same frequency: 20Hz
However, this is not mandatory: controller and pusher can also work at a different frequency.
Dummy camera node generates an image every 2 seconds, so it works at the frequency of 0.5Hz